## Slide 1: The Reuleaux Library for WorkSpace Analysis
Abhijit Makhal
PhD Student
Idaho State University

## Slide 2: Why do we need Analysis of Workspace??
Deduction for the robot/ user about the reachable places
Abstraction for the arm’s capability suitable for task planners, path planners and grasp planners
Where the hand tool center points (TCP) can be easily reached and where not
Visualize directional and structural information about the workspace imposed by robot design
Base placement : Especially for multiple pick and place locations

## Slide 3: Current Solutions
moveit workspace analysis
  https://github.com/ros-planning/moveit_advanced/tree/indigo-devel/moveit_workspace_analysis
  https://www.youtube.com/watch?v=OglpJnElgu4
  No structural definition of workspace, analysis can only be done by defining end-effector goals
  Cannot directly solve base-placement
  No stable release
  No available documentation
  Implementation level – currently not known

## Slide 4: Current Solutions
OpenRave KinematicReachability Module
OpenRave InverseReachability Module
  No user-friendly documentation available
  No structural synthesis
  No user-defined arguments
  The data from the map is not reusable for other applications
  No ROS-support (openrave_planning package non-existent after ROS Fuerte)
  Map generation time for a 6DOF robot varies from 2-3 hours
  Size of the map file varies from 150 – 200 mb
  Implementation only in base-placement, still the process takes more than 3 hours for single object/grasp location

## Slide 5: Current Solutions
DLR method for reachability/capability
No ROS-support
Map generation process takes upto 7-8 hours/ Higher DOF
arm has taken 13 hours
Size of the file of the map 150 – 200 mb
Own custom file structure for maps
User-friendly Documentation available
Structural and directional synthesis available
Implementation in motion planning, grasp planning and
base-placement
http://robotics.estec.esa.int/ASTRA/Astra2015/Papers/Session%206A/96089_Porges.pdf
http://link.springer.com/chapter/10.1007%2F978-3-319-03653-3_50

## Slide 6: Our Method
OpenRave KinematicReachability + DLR method
REULEAUX
ROS-support
Structural and directional synthesis
Based on existing ROS structure and robot representations
Scope of user argument as per application needs
Easily readable map structure
Map size ranges from kb-25 mb
Approximate map generation time ~ 5-15 min
Can be easily extended to applications such as grasp planning, motion planning or base-placement

## Slide 7: How Reuleaux works?
Environment
Voxelization
1
2
Sphere
Discretization
3
Pose
Generation
4
Pose
Collection
5
Pose
Filtering

## Slide 8: How Reuleaux works?
Reachability Map
  Stores All the Filtered Sphere Coordinates and Reachable Poses
  Based on Reachability Index
  R = Number of valid Ik solutions on the Sphere
  N = Total number of Poses on the Sphere
Capability Map
  Captures the directional information
  For the outer spheres try to fit a cone with Shape Fir Error(SFE)
  R = Number of valid Ik solutions on the Sphere
  r = Number of poses the cone fails to cover
  u = Number of poses the cone wrongly covers
[1] F. Zacharias, C. Borst and G. Hirzinger, "Capturing robot workspace structure: representing robot capabilities," 2007 IEEE/RSJ International Conference on Intelligent Robots and Systems, San Diego, CA, 2007, pp. 3229-3236.doi: 10.1109/IROS.2007.4399105
[ 1]
[ 1]

## Slide 9: Visualization
Dissections
By Reachability Index
Change Sphere Color
Show Reachable Poses

## Slide 10: Results
Resolution | Number of Voxels | # of Reachable Spheres | # of Reachable Poses | Time | File Size
0.5 | 64 | 8 | 71 | 0s | 10.9 kb
0.25 | 343 | 35 | 541 | 1s | 30.6kb
0.1 | 3375 | 294 | 8423 | 1s | 354.2kb
0.08 | 6859 | 543 | 16527 | 3s | 686.3kb
0.035 | 79507 | 5536 | 196568 | 29s | 8mb
0.025 | 226974 | 14652 | 538910 | 95s | 22mb
Reachability Map
Capability Map
Resolution | # of Reachable Spheres | Time | File Size
0.5 | 8 | 42s | 3.1 kb
0.25 | 35 | 106s | 5.2kb
0.1 | 294 | 412s | 26 kb
0.08 | 543 | 731s | 45.9kb
0.035 | 5536 | 5012s | 445.3kb
0.025 | 14652 | 11939s | 1.2mb

## Slide 11: Future Work
Project Continuation:
Base Placement for specific tasks by Inverse Reachability
Potential Future works
  Better Visualization
  Support for 7+ dof robots
  Singularities, Joint Limits
can you place the robot/object in such a way so as to avoid/minimize object refixturing?

## Slide 12: https://github.com/ros-industrial-consortium/reuleaux
Questions Please