## Slide 1: ROS-I Meeting 09/08/2016 Reactive and Adaptive Path Planning
GSoC 2016 student
www.kentaro.wada@gmail.com
Kentaro Wada

## Slide 2: Reactive and Adaptive Path Planning
Situations that needs this planning:
  Unknown environment.
  Few sensors.
  Many occlusions.
Inputs for reactive/adaptiveness:
  Sensor input.
  User operation.
For reactive and adaptive planning:
  "Reactive" + "Adaptive" =
  "Stop execution" + "Re-planning"
Simulator
Robot
Planner
Sensors
Joint Trajectory
Sensor Input
Controller
Planning
User
User Input
Stop and Re-plan
Plan for goal
Joint Trajectory
System of reactive path planning with simulated robot

## Slide 3: Request stops during trajectory execution
Situations about stop requests:
  Request by operator for unexpected sensor input.
  Request from controller for unexpected sensor input.
Required Features:
  GUI for operator's stop request on Rviz. (Fig. 1)
    This is completed and merged in moveit_ros.
  Monitor planned joint trajectory execution.
    Currently MoveIt! does not have a ROS action for execute trajectory, in spite of the necessity of monitoring for canceling.
    https://github.com/ros-planning/moveit_ros/pull/719
Figure 1: GUI for operator's stop request.

## Slide 4: Re-planning after stopping execution
Situations about re-planning:
  Re-plan by operator.
  Re-plan considering about the sensor inputs before.
Required Features:
  None.
  Updating the planning scene or octomap.
    Fix MoveIt! planning scene which is not updated after trajectory execution.
    https://github.com/ros-planning/moveit_ros/issues/711
    Fix octomap generation with force sensor which currently won't work. (Fig. 2)
    https://github.com/jsk-ros-pkg/jsk_recognition/issues/1834
Figure 2: Octomap generation with contact.
(https://github.com/jsk-ros-pkg/jsk_recognition)

## Slide 5: Demonstration 1: Reactive and Adaptive Path Planning with Operator Input
Situation:
Robot in front of the shelf.
Shelf position can be mis-calibrated.
Visualization for operator:
Force sensor input.
MoveIt! planning, execution and stopping.
Initial State
Plan
Execute
Stop
Goal
Goal:
Robot insert end-effector to the narrow space.
Pick
(not yet)
Insert
(done)
Place
(not yet)

## Slide 6: Demonstration 2: Reactive and Adaptive Path Planning with Sensor Input
Situation:
Robot in front of the shelf.
Shelf position can be mis-calibrated.
Visualization:
Force and RGB-D sensor input.
Voxel grid mapping with octomap.
Initial State
Plan
Execute
Stop
Goal
Goal:
Placing the target object in bin.
RGB-D sensors
Force sensor
Pick
(not yet)
Insert
(not yet)
Place
(not yet)

## Slide 7: Next plans
Complete required features for reactive and adaptive planning for being merged to the origin.
Complete demonstration with operator input:
  Complete whole system: "stow task: moving object from bin to shelf".
  Complete vacuum gripper and object simulation.
Complete demonstration without operator input:
    Complete whole system: "pick task: moving object from shelf to bin ".
    Complete planning with scene updates with a force sensor.